## Slide 1: Reflected Waves
AE 2010:
Thermodynamics and Fluids Fundamentals

## Slide 2: Reflected Waves
Already examined what happens when normal shock “hits” a boundary
  If incident shock hits solid wall, get reflected (normal) shock – required to satisfy velocity (B.C) boundary condition (v=0)
  If it hits open end, get reflected expansion waves – satisfy pressure B.C. (P=Pa<P2)
Wave reflections “impose” B.C. (pressure or velocity) on flow
vs
vg
vrs
vg
v=0
vs
vg
pa
vg
pa
p2

## Slide 3: Oblique Shock Reflection From Wall
Consider “weak” (M2>1) oblique shock wave impinging on a flat wall
  Incident shock wave turns flow toward the lower wall
  Flow can not pass through boundary, must turn back parallel to lower wall – velocity boundary condition
  Flow turns back on itself  compression in this case, reflected wave is oblique shock
Reflected shock weaker than incident shock
  M2<M1
M2
M1
d1
qi
M3
qr

## Slide 4: Example: Oblique Shock Reflection
Given: Mach 3.2 flow with static pressure of 25 psia approaching a 17o (d1) turn produces oblique shock wave at 33o (q1). Oblique shock then “hits” bottom wall, producing reflected oblique shock.
Find: qi, qr, M2, M3, P2, P3
Assume: TPG/CPG with g=1.4, steady, adiabatic, no work, inviscid except shocks,
M2
M1
d1
qi
M3
qr
p1
q1

## Slide 5: Example: Oblique Shock Reflection
Analysis:
  M2, p2
  qr
with M1n, B or eqs.
  M3, p3
flow must be turned horizontal again, so d2=d1 =17°
M2=2.29 table or Eq.
with M2n, B or eqs.
M3
M2
M1=3.2
d1=17°
qi
qr
p1=25 psia
33°=q1
  qi
 qi
d2
q2

## Slide 6: Mach Reflection
If M2 low enough, required turning angle for reflected wave may exceed maximum oblique shock angle
  No simple reflected wave possible, get something like detached shock
  IO: incident oblique shock
  OW: strong curved shock, normal at wall
  OR: weak oblique shock
M2
M1
M>1
O
R
I
M<1
W

## Slide 7: Oblique Shock and Pressure BC
If oblique shock “hits” a pressure boundary condition, reflected wave must adjust flow pressure to match boundary pressure
Type of reflected wave will depend on whether pressure must drop or rise
  Pressure rise  compression: flow will “turn back on itself”
  Pressure drop  expansion: flow will “open up”

## Slide 8: Reflection From Expansion on Wall
Consider PM fan impinge on a flat wall
  Incident expansion waves tend to turn flow away the lower wall
  Can not create vacuum, flow must be turned back parallel to lower wall – velocity boundary condition
  Flow “open up”  expansion  in this case, reflected waves are expansions (Mach waves)
M3
M2
M1
d1=2-1

## Slide 9: Non-Simple Region
M3
M2
M1
In region where incident and reflected waves interact, can not use our simple quasi-1D theory
In this non-simple region,
  Get curved waves
  Flow still isentropic
Outside this region, our quasi-1D methods still valid
Non-simple region
(magnified here)

## Slide 10: Summary of Reflected Waves
“Reflections” from supersonic waves represent information from a boundary being transmitted into supersonic flow
  reflections “impose” boundary condition on flow
Generally, pressure or velocity boundary conditions
Type of reflected wave will depend on whether compression or expansion is needed to meet boundary conditions