## Slide 1: Starting Problem
AE 2010:
Thermodynamics and Fluids Fundamentals

## Slide 2: Supersonic Windtunnels
For supersonic wind tunnels, closed circuit tunnel requires less power to operate then open tunnels
  Do not have to accelerate flow as much
Use two CD nozzles (really nozzle and diffuser)
  Need subsonic flow (compressors)
  Less Po loss than using shock to get subsonic flow
M>1
M<1
M<1
Test Section
Compressor
Nozzle
Diffuser

## Slide 3: Starting Problem
What happens during tunnel startup
  No initial velocity
  Pressure uniform throughout tunnel
  Start tunnel by changing Po/Pb using compressor
As raise Po/Pb, start with subsonic flow everywhere
  Eventually reach M=1 at 1st throat (if At1≤At2)
M<1
po
pb
Compressor
Test Section
pb
p*/po
x
p/po
1
M<1
M<1
M=1
A t1
A t2
M<1
Mtest<1

## Slide 4: Starting Shock
Further increase in Po/Pb
  Normal shock in diverging section of nozzle
Can At2=At1?
  A* increase across shock (A2*/A1* ~Po1/Po2)
  To get same mass flowrate through 2nd throat, At2>At1
How big does At2 have to be?
  Biggest Po loss for strongest shock  shock in test section
M<1
M<1
=1
A t1
A t2
M<1
>1
g=1.4

## Slide 5: Swallowing Shock
So raise Po/Pb until shock enters test section
  M in test section, M2 after shock
To have shock “disappear”, must pass through 2nd throat
  At2=A2* at M2 after shock at Mtest
  Increase Po/Pb slightly above previous case
  Shock leaves test section, enters “diffuser”
  A2* drops (M drops); shock keeps going; shock swallowed
M<1
=1
A t1
A t2
>1
<1
M<1
=1
M1=Mtest
M2 <1
=1
A t1
A t2
M<1
>1
>1
>1
M=Mtest>1

## Slide 6: Operating Conditions
Want to run tunnel with lowest power requirements
  Lowest Po loss
  Operate with weakest shock possible
Fixed diffuser throat area
  Weakest shock (M lowest) when it is at diffuser throat
  More stable operation (for Po/Pb variations) if shock just downstream of throat
Variable diffuser throat area
  Lowest Po loss for no shock (M=1)
  Reduce At2 to At1 (stability, At2=At1+∆)
M<1
=1
A t1
A t2
>1
M>1
>1
Mdesign>1
A t2
<1
M>1
>1
A t2
<1
M>1
=1

## Slide 7: Example: Windtunnel Design
Given: supersonic windtunnel designed to run on N2 and operate at Mtest=3, 1 m2 test section
Find
  Minimum diffuser throat area to start tunnel, i.e., get supersonic flow in test section
  Maximum Po loss during startup
  Minimum Po loss during operation for fixed area diffuser
Assume: TPG/CPG with g=1.4
M>1
po
pb
Compressor
Test Section

## Slide 8: Solution: Windtunnel Design
Analysis: Diffuser throat
  During startup, diffuser throat must be just large enough to handle total mass flowrate with Po2 after strongest shock (in test section)  Ath,D=A2*
Isen.
shock
M1=3
Ath,N
Ath,D
po1
po2
M2

## Slide 9: Solution: Windtunnel Design
Analysis: Pressure Losses
  During startup, max. Po loss for strongest shock  in test section
  During operation, min. Po loss for weakest shock  at diffuser throat  need M at throat (M1, A>A1*)
M1=3
Ath,N
Ath,D
po1
po2
M2
A th,D
<1
M>1