## Slide 1: Strong and Weak Oblique Shocks
AE 2010:
Thermodynamics and Fluids Fundamentals

## Slide 2: Strong and Weak Oblique Shocks
As we have seen, it is possible to get two solutions to equation
  2 possible values of q for given (d,M1)
  e.g.,
Examine graphical solution
M1=2.4
39.4°
M2=1.75
d=16°
M1=2.4
82.1°
M2=0.575
d=16°

## Slide 3: Graphical Solution
=1.4
M2<1
M2>1
Strong
Weak
=sin-1(1/M1)
d (deg)
q (deg)
Weak shocks
  Smaller q
  qmin=m
  Usually M2>1
Strong shocks
  qmax=90o (normal shock)
  Always M2<1
Both for d=0
No turn for normal shock or Mach wave

## Slide 4: Which Solution Will Occur?
Depends on upstream versus downstream pressure
  e.g., back pressure
  P2/P1 large for strong shock, small for weak shock
Internal Flow
  Can have P2 much higher or close to P1
External Flow
  Downstream pressure usually close to upstream P (both near Patm)
M>1
p1
pb,high
M>1
p1
pb,low
M>1 patm
patm

## Slide 5: Maximum Turning Angle
Given M1, no straight oblique shock solution for d>dmax(M)
Given d, no solution for M1<M1,min
Given fluid (g), no solution for any M1 beyond dmax e.g., ~45.5o (g=1.4)
=1.4
dmax(M=3)~34°
dmax()
d (deg)
q (deg)

## Slide 6: Detached Shock
What does flow look like when no straight oblique shock solution exists?
  Detached shock/bow shock, sits ahead of body/turn
  Normal shock at centerline (flow subsonic to negotiate turn); curves away to weaker shock
M1>1
q>qmax
bow shock can cover whole range of oblique shocks (normal to Mach wave)
asymptotes to Mach wave
M2<1
M2>1
M1>1
q>qmax