## Slide 1: Supersonic Inlet
AE 2010:
Thermodynamics and Fluids Fundamentals

## Slide 2: Supersonic (Engine) Inlets
For air-breathing engines on supersonic vehicles, usually want to slow flow down to subsonic speeds inside engine
  Need diffuser (M>1M<1) for engine inlet
  Exception: supersonic combustion (e.g., SCRAM jets)
Goal
  Lowest Po loss (highest thrust)
    Given flight M
    Mass flow rate requirement (thrust)
    Stable operation (nothing drastic for small changes in flight conditions)

## Slide 3: CD Inlet
Can get close to isentropic flow
  lowest potential po loss
  starting problem, M<Mdesign like supersonic wind tunnel, have to swallow shock
    can be done by overspeeding: fly above Mdesign until shock sits at entrance
    usually requires variable area throat or bypass valves (heavy, complex)
  stability problem: if “shock” leaves throat, lowering mass flow (higher A2*)
Not typically used
+ M
M>1
M<1

## Slide 4: Shock Inlets
Normal shock diffuser
  Simple, diverging section preceded by normal shock
  Highest Po loss (strong shock)
Oblique Shock Diffuser
  Oblique shocks followed by normal shock at (or inside) inlet to subsonic diffuser
  Lower Po loss
  Works for range of M

## Slide 5: Example: Normal vs. Oblique Diffusers
Given: You need to pick a diffuser for Mach 2 flight conditions. Your choices are a normal shock diffuser and 2 different oblique shock diffusers
Find: stagnation pressure loss for each (Po,final/Po,initial)
Assume: air is TPG/CPG with g=1.4, stead, adiabatic, no work, inviscid except for shock
M=2
20°
M=2
10°
5°
M=2
po,initial
po,final
po,final
po,initial
po,final
po,initial

## Slide 6: Solution: Normal vs. Oblique Diffusers
Analysis:
  Normal shock diffuser
  Single oblique shock (+normal)
B.1
B.1
Normal shock inlet – 28% Po loss
Oblique shock inlet – 13.3% Po loss
M1=2
po1
M2, po2
20°
M1=2
M2, po,2
po1
M3, po3

## Slide 7: Solution: Normal vs. Oblique Diffusers
Analysis:
  Two 5o turns (+normal shock)
B.1
C.1
B.1
B.1
Double oblique shock inlet – 12.7% Po loss
M2, po,2
po1
M3, po3
10°
5°
M=2

## Slide 8: Double Oblique Inlet - Advantages
So for M=2, same total turning angle (10o)
  Two oblique shocks slightly better than one (12.7% vs. 13.3% Po loss)
  Significant improvement over normal shock alone (28% Po loss)
Oblique shock diffuser with two 10o turns (total d of 20o) even better
  Only 4.3% Po loss (solution shown on next slide)
  So larger overall deflection can give better Po
Stagnation pressure advantages of using multiple oblique shocks increase with higher M

## Slide 9: Double Oblique Shock Diffuser
From previous results for 10o turn
Two 10o turns (+normal shock)
M2, po,2
po1
M3, po3
20°
10°
M=2

## Slide 10: Double Oblique Inlet - Disadvantages
Flow separation
  Since P increases across oblique shocks, the flow sees adverse P gradient
  So more or bigger oblique shocks (or longer external ramp), the greater the chance the boundary layer will separate  major change in flow field, large losses (Po and mass flow rate)
Internal Turn Angle
  Larger total external turn angle showed less Po loss
  Larger external flow turning requires larger inlet
  Also requires larger internal flow turning to get flow back to horizontal
Bleed Air
Oblique Shocks
Normal Shock
Spilled Air
BypassAir
Subsonic Diffuser
Boundary Layer