## Slide 1: Under and Over Expansion
AE 2010:
Thermodynamics and Fluids Fundamentals

## Slide 2: Under/Over Expanded Nozzles
Recall previous analysis of CD nozzles, e.g., as back pressure is reduced
Have looked at range of Pb that produce
  Isentropic solutions or
  Shocks in nozzle
What happens when
  Pb < Pes,sup (U)
  Pes,sup< Pb< Pe,sh (O)
pb
pe
po To
Ae
At
pes,sup
p*/po
x
p/po
1
x
M
1
Mes,sup
Mes,sub
pes,sub
pe,sh
Me,sh
M<1, isen.
M<1, shock
U
O

## Slide 3: Under Expanded Nozzles
Start with Pb<Pes,sub
  Under expanded case
  Pe>Pb (not enough expansion has occurred)
So boundary condition at exit requires a supersonic expansion process
  2-D Prandtl-Meyer flow
  Flow turns, pressure drops to back pressure
  But flow must not cross centerline (symmetry line; like a wall)
pes,sup
p*/po
x
p/po
1
pes,sub
pe,sh
M<1, isen.
M<1, shock
U
p1=pe
pb
p2=pb
C
L

## Slide 4: Centerline Boundary Condition
Centerline
  Flow along centerline must be parallel to centerline
  To get flow to turn inward again requires another PM expansion
  But second expansion means pressure in region 3 drops below back pressure (P3<P2=Pb)
  So now we will need to do something to match our pressure boundary condition at the edge of the jet
nonsimple region
p1>pb
pb
p2=pb
C
L
1
2
3
p3<pb

## Slide 5: Jet Boundary Condition
Jet boundary
  Along “edge” of jet must satisfy pressure B.C.
  To match pressure, P must rise  compression
  Can get PM compression waves
  Combine to form oblique shocks, turn flow inward
  Centerline (velocity) boundary condition requires reflected compression waves
  Now pressure exceeds surrounding pressure (P5>Pb), away we started, so process/cycle repeats itself
p1>pb
pb
p2=pb
C
L
1
2
3
p3<pb
4
p4=pb
5
p5>pb
slip line

## Slide 6: Under Expanded Jet
For Pe>Pb, nozzle produces a jet flow consisting of regions of decreasing and increasing P (or density)
  Inviscid flow (ideal), process would continue endlessly
  Viscous case (real), viscous losses and turbulent mixing with surroundings causes wave pattern to decay after small number of cycles
p1>pb
p2=pb
C
L
1
2
3
p3<pb
4
p4=pb
5
p5>pb

## Slide 7: Over Expanded Nozzles
Pes,sup<Pb<Pe,sh
  Over expanded case
  Too much expansion has occurred
So boundary condition at exit requires a supersonic compression process
  Oblique shock (2-D)
  Flow turns, pressure rises to back pressure
  Flow must not cross centerline, so get reflected shocks
  Then expansion to match P, etc.
pes,sup
p*/po
x
p/po
1
pes,sub
pe,sh
M<1, isen.
M<1, shock
O
p1<pb
pb
p2=pb
C
L
p3>pb

## Slide 8: Over Expanded Jet
For Pe<Pb, nozzle produces jet flow consisting of regions of increasing and decreasing pressure (or density)
  Same pattern as for under expanded case, just “out-of-phase” (compressions first, then expansions for over expanded vs. expansions then compressions for under expanded)
p1<pb
C
L
1
2
p3>pb
3
p2=pb
p4=pb
4
5
p5<pb

## Slide 9: Mach (Shock) Diamonds
Regions of high pressure, also have high density (and temperature)
  These hot, dense gases emit light (radiation)
p1>pb
p2=pb
C
L
1
2
3
p3<pb
4
p4=pb
5
p5>pb